## Slide 1: VMWare Workstation Hypervisor – Case Study
Dr. Amit Praseed

## Slide 2: Overview of VMWare Workstation
VMWare Workstation is a type 2 (hosted) hypervisor
  Runs on a host operating system
Design Goals
  Provide the traditional benefits of virtual machines
  Virtualize x86 PCs
  Run like an application
  Run with good performance
Hardware
Operating System
VMWare Workstation
Native Application
VM
Guest OS
App

## Slide 3: Requirements of VMWare
Virtualization techniques require
  Access to privileged CPU state
  Complete control of the Memory Management Unit (MMU)
The Host OS gets in our way
Need to both run as an application and as a privileged virtual machine monitor

## Slide 4: 3 – Component Model
Hardware
Host Operating System
VMWare Workstation
Native Application
VM
Guest OS
App
VMM
Switch to privileged VMM to run virtual machine
  VMM takes complete control of CPU and MMU
  Host OS state is saved / restored on switch

## Slide 5: Resource Usage by VMWare
Host OS assumes it is in control all the time
VMM takes control for a bounded amount of time
Each VM is controlled by a distinct VMM instance
Distinct process instance of host OS – VMX
Kernel Resident Driver: Responsible for locking memory pages, forwarding interrupts, world switch etc.
Interrupts are handed over to the host OS for handling

## Slide 6: CPU Virtualization
Traditional virtualization technique
  Direct Execution
  Run OS at an unprivileged CPU level
  CPU traps to VMM on privileged instructions
  VMM emulates privileged instruction
However, x86 is not strictly virtualizable (Why?)

## Slide 7: Solution : Binary Translation
  Inspects each instruction before its executed
  Replaces “dangerous” instructions with calls to emulation code
  Stores sequences of translated instructions in a translation cache
  Fast, but slower than direct execution

## Slide 8: Dual Virtualization Method
Use traditional direct execution when possible
  Well behaved user-level programs
Use binary translation when not
  Operating system
  Real mode programs (old 16 bit DOS apps)
  User-level programs with special privileges

## Slide 9: Proportional Share (Lottery) Scheduling
One very basic concept: tickets
  Represent the share of a resource that a process should receive.
  The percent of tickets that a process has represents its share of the system resource in question
Achieved probabilistically by holding a lottery every so often
Holding a Lottery:
  the scheduler must know how many total tickets there are
  Scheduler picks a winning ticket
  Whichever process holds the ticket wins
  Probabilistic correctness in meeting the desired proportion, but no guarantee

## Slide 10: Memory Management
Protecting the VMM:
  The VMM address space needs to be protected from other VMs
  Segment Truncation
    Only restricts the limit – hence VMM needs to be in the top 4 MB of memory
Host physical memory is managed by VMX process
  Locks required pages in memory
  Shadow Paging to ensure that guest OS only request valid pages

## Slide 11: Device Management
Hosted hypervisors can utilize the device drivers in the underlying OS
  I/O requests are remote procedure calls between VMM and VMX
  VMX issues system calls to the host OS
  Interrupts generated within the guest OS are handed over to the host OS
  Executed as if VMX thread has issued the interrupt

## Slide 12: Device Usage by VMWare
Hardware
Host Operating System
VMWare Workstation
Native Application
VM
Guest OS
App
VMM
Device I/O is routed through the application
Use standard OS system call interfaces